## Slide 1: Multimodal Sensing-Assisted User Association and Tracking in Vehicular Networks
Yifeng YUAN · MPhil in Internet of Things
Supervisors: Shijian GAO and Jia YAN · June 2026

## Slide 2: V2I Beam Alignment
Narrow beams provide the array gain required by high-frequency V2I links, but vehicle motion, blockage, and path evolution rapidly age beam and CSI information.
Repeated SSB and CSI-RS measurements improve reliability. The same measurements consume resources otherwise available for data. Measurement reliability ↔ Measurement overhead

## Slide 3: Target-to-User Association
A target-level beam prediction is useful only when it is applied to the intended communication user.
Visible vehicles, active VUEs, and maintained tracks are not naturally one-to-one.
SENSING DOMAIN
Physical vehicles
Detections
Perception tracks
COMMUNICATION DOMAIN
VUE identities
Beam measurements
Downlink transmission
Which track corresponds to which VUE?

## Slide 4: Research Objectives and Contributions
Objective Close the sensing-to-communication loop while reducing beam-measurement overhead and preserving user-specific decisions.
Perception → Association → Communication evaluation
1 Distributed multimodal BEV perception and beam prediction Joint vehicle detection and per-target CSI beam classification. 2 Target-to-user association with IMM-based tracking Beam measurements establish associations; tracking preserves target continuity. 3 Multimodal V2I simulation and NR-oriented evaluation One chain connects sensing use, fallback, overhead, and effective user rate.

## Slide 5: System Model
01
What information is available to the BS, and how does a beam candidate affect user rate?

## Slide 6: Network and Sensing Model
The target BS combines BS-local ISAC sensing with distributed camera coverage from neighbouring sensing nodes.
Target BS b serves U_b[n] Neighbouring nodes add viewpoints but not communication cells All inputs are aligned in the target-BS BEV frame O_b,n = {I_b,n, I_Nb,n, P_b,n}

## Slide 7: Communication and Rate Model
Candidate beams affect both the measured channel and the resources remaining for data transmission.
Missing a useful beam reduces SINR; measuring fewer successful candidates increases the data-resource fraction.
SSB coarse direction → CSI-RS candidate measurement → CSI feedback → RZF precoding and data Selected measured beam k* = arg maxₖ γ̂ᶜˢⁱ(k), k ∈ 𝒞(b,u,n) Effective user rate Rᵉᶠᶠ = ηdata B ηDL log₂(1 + γRZF)

## Slide 8: Design Requirements
A sensing-assisted beam-management policy must respect three information boundaries.
No oracle VUE identity · No direct service-beam declaration
1 TARGET-LEVEL PREDICTION Predict beams for an observed physical target, not a known VUE. 2 MEASUREMENT-GROUNDED ASSOCIATION Establish which perception track belongs to each VUE. 3 MEASURED SERVICE-BEAM SELECTION Use sensing to narrow CSI-RS candidates; use measured quality to select service.

## Slide 9: Proposed Framework
02
How does unbound sensing evidence become a VUE-specific CSI-RS decision?

## Slide 10: DMSA-BM Architecture
Multimodal observations → detections and beam posteriors → physical-target tracks → VUE-track associations → CSI-RS candidates
1 DISTRIBUTED MULTIMODAL PERCEPTION
Cameras + BS-local ISAC
Vehicle detections
Per-target beam posteriors
2 IMM-BASED TRACKING
CV and CT motion models
Detection-to-track assignment
Physical-target continuity
3 TARGET-TO-USER ASSOCIATION
VUE-indexed beam measurements
One-to-one matching
Accepted or unmatched
4 CANDIDATE MEASUREMENT
Accepted + observed
Top-K predicted beams
Otherwise
SSB-guided refinement

## Slide 11: Cross-Node Fusion
Cross-node attention selects complementary viewpoints at each BEV location while preserving the target-BS perspective.
Target-BS-conditioned queries preserve the serving-link view; geometry-aware keys distinguish node locations; masks exclude invalid projections.
Target-BS BEV
Node 1 BEV
Node 2 BEV
···
Validity masks
GEOMETRY-AWARE
MASKED ATTENTION
αⱼ(x) = softmaxⱼ
[q(x)ᵀkⱼ(x)/√d + b(gⱼ→b)]
Target-BS-centred
distributed camera BEV
Neighbouring evidence dominates only where valid.

## Slide 12: Multimodal Fusion
Gated local and global attention adapt camera–ISAC fusion to spatial and scene-wide observation conditions.
The fusion weights are learned from sensing features; availability masks only exclude missing inputs.
CAMERA BEV
Semantics and visibility
ISAC BEV
Complementary geometry
GATED ATTENTION
βq(x) ∝ exp
[ℓlocal,q(x) + ℓglobal,q]
Availability mask
FUSED BEV
Local weights respond to occlusion and sparsity.
Global weights respond to illumination and visibility.

## Slide 13: Joint Detection and Beam Prediction
A shared BEV representation produces vehicle detections and a per-target posterior over 192 CSI beams.
Detection output r̂ᵢ, attributes, confidence Beam output pᵢ = softmax(logits at r̂ᵢ) Training Top-1 cross-entropy Use Full posterior retained for ranking

## Slide 14: IMM-Based Tracking
IMM estimation preserves physical-target continuity across straight and turning motion.
CV state [x, y, vₓ, vᵧ]ᵀ CT state [x, y, v, ψ, ω]ᵀ IMM cycle Mix → predict/update → mode likelihood → fuse Mahalanobis gating + Hungarian assignment

## Slide 15: Initial Target-to-User Association
Conventional beam measurements anchor the mapping between VUE identities and currently observed tracks.
Feasible pair Current observation SSB-parent consistency Accepted association Low cost + sufficient margin One-to-one assignment Unmatched option retained
VUE-INDEXED EVIDENCE
VUE 1 measured beam κ₁
VUE 2 measured beam κ₂
···
VUE U measured beam κᵤ
Serving SSB parent
TRACK-INDEXED POSTERIORS
cᵤᵣ = −log[pᵣ(κᵤ)+ε]
──────────────
log MCSI
Filter infeasible pairs
Form bipartite cost matrix
ONE-TO-ONE ASSIGNMENT
Hungarian matching
+ unmatched option
Accept only if
• cost ≤ threshold
• margin ≥ threshold
Otherwise remain unbound

## Slide 16: Candidate Beam Selection
Only an accepted association with a current observation can reduce the CSI-RS scan.
In both branches, the service beam is selected from measured CSI-RS quality.
Accepted VUE–track pair
AND
current target observation?
YES
Top-K posterior beams
or adaptive cumulative-mass set
(minimum Top-1)
NO
SSB-guided CSI-RS refinement
(conventional fallback)

## Slide 17: Algorithm Summary
The framework separates sensing computation from air-interface measurement cost.
Scaling drivers Views and BEV resolution · targets and tracks · assignment size · M_CSI · K_scan
1 Construct distributed multimodal BEV features. 2 Decode detections and beam-class posteriors. 3 Predict, assign, and update physical-target tracks. 4 Reassociate only when an association event occurs. 5 Select sensing-derived or SSB-guided CSI-RS candidates.

## Slide 18: Experimental Evaluation
03
Does the complete decision chain improve communication performance after measurement cost is included?

## Slide 19: Experimental Setup
A common multimodal and communication protocol links perception results to effective user rate.
SCENARIOS
Four roadside BSs
Clear
Rain/Fog
Night
Disjoint train, validation, and test sequences
MULTIMODAL DATA
Target-BS cameras
Neighbouring-node cameras
BS-local ISAC point clouds
Vehicle trajectories
Ray-traced channels
RADIO PROFILE
48 SSB beams
192 CSI-RS beams
SSB period 100 ms
CSI-RS period 20 ms
Common power, noise, Doppler, RZF, and overhead accounting
EVALUATION CHAIN
Detection
→ Beam ranking
→ Association-conditioned use
→ CSI-RS overhead
→ Effective user rate
Rain/Fog margin is a fixed test-tuned operating point.

## Slide 20: Perception and Beam Prediction
Distributed multimodal attention improves target availability without uniformly dominating every beam-ranking metric.
Chart: 
| AP@2m | Recall@2m | Beam Top-1 | Beam Top-4
Local camera–ISAC fusion | 74.35 | 79.53 | 71.54 | 94.66
Distributed multimodal attention | 78.73 | 81.51 | 71.13 | 94.13
Blue Distributed multimodal attention
Gray Local camera–ISAC fusion
Proposed
AP 78.73%
Recall 81.51%
Top-4 power ratio 97.01%
Local fusion
Top-1 71.54%
Top-4 94.66%
Target observability and beam ranking are distinct objectives.

## Slide 21: Cooperative Sensing Nodes
Additional roadside viewpoints primarily improve detection and localisation.
Blue AP@2m Orange Recall@2m Olive Beam Top-4@2m Fixed trained model Available nodes varied only at test time 0 → 5 nodes AP 38.59% → 80.41% Recall 52.34% → 83.15% Beam Top-4 approaches saturation.
Chart: Available nearby sensing nodes
| 0 | 1 | 2 | 3 | 4 | 5
AP@2m | 38.59 | 50.3 | 56.42 | 58.39 | 71.4 | 80.41
Recall@2m | 52.34 | 57.39 | 60.78 | 62.45 | 74.25 | 83.15
Beam Top-4@2m | 91.58 | 92.03 | 94.09 | 94.63 | 95.3 | 95.4

## Slide 22: Ablation and Tracking Results
Local multimodal complementarity provides most of the gain; distributed sensing improves the final operating point.
CSI-RS overhead Camera 1.86% ISAC 1.81% Local fusion 1.80% DMSA-BM 1.56% Tracker check IMM 146.332 KF-CV 146.373 KF-CT 145.880 Mbps Similar rates do not establish universal IMM superiority.
Chart: Mean effective user rate (Mbps)
| Camera-only | ISAC-only | Local camera–ISAC | DMSA-BM
Effective user rate | 138.868 | 142.522 | 143.701 | 146.332

## Slide 23: Conclusion
04
What has been established, and what remains before deployment?

## Slide 24: Conclusions and Future Work
Distributed sensing becomes useful for beam management through a user-specific measurement interface.
NEXT STEPS Real-world validation Protocol-level NR evaluation Online and domain adaptation Cooperative multi-BS association QUESTIONS AND DISCUSSION
□ Distributed multimodal BEV perception jointly detects vehicles and ranks per-target CSI beams. □ IMM tracking preserves physical-target continuity without treating a track as a VUE identity. □ Beam measurements establish target-to-user associations; only accepted, currently observed pairs reduce CSI-RS scanning. □ Under the stated operating point, DMSA-BM achieves 146.332 Mbps with 1.56% CSI-RS overhead.