## Slide 1: Multimodal Sensing-Assisted User Association and Tracking in Vehicular Networks
Yifeng YUAN · MPhil in Internet of Things
Supervisors: Shijian GAO and Jia YAN · June 2026
Notes: Introduce the thesis question: when can roadside sensing safely reduce beam measurements for the intended V2I user?

## Slide 2: Background
Connected mobility and intelligent transportation rely on reliable V2I connectivity.
Vehicular networks connect moving vehicles, roadside infrastructure, and network services.
Roadside operating conditions
High mobility · rapidly changing geometry · intermittent blockage
Communication requirements
High data rate · low latency · reliable connectivity
Notes: Start from the application setting. Vehicular networks must support high-throughput, low-latency, reliable roadside connectivity despite fast motion and changing geometry.

## Slide 3: V2I Beam Management Problem
High-frequency V2I links use narrow beams to obtain array gain. Mobility, blockage, and path evolution rapidly age beam information.
More frequent or wider CSI-RS measurements improve alignment reliability, but consume time-frequency resources.
Measurement reliability ↔ Measurement overhead
SSB access
CSI-RS candidates
CSI feedback
Data transmission
Notes: Explain that narrow beams are valuable but require recurrent SSB and CSI-RS actions. The tension is reliable alignment versus measurement overhead.

## Slide 4: Sensing-Assisted Beam Prediction: Single-Candidate Scenario
Multimodal sensing can predict or rank beams for a known physical target.
Camera · position · radar · LiDAR → physical-scene observations
Single-candidate assumption: a specified or visually isolated target is treated as the intended communication user.
Beam prediction: fθ(O[n]) → Top-K candidates
Prediction narrows the CSI-RS search; measured CSI quality selects the service beam.
Known physical target
Multimodal scene observation
Top-K beam candidates
Notes: Explain the common single-candidate formulation: once the physical target is known, multimodal scene observations can produce a short beam list.

## Slide 5: Sensing-Assisted Beam Prediction: Multi-Candidate Scenario
When several vehicles are visible, prediction must first identify the intended transmitter.
User-conditioned prediction: fθ(O[n], g[u,n]) → VUE-specific Top-K beams
O[n]: scene-level sensing observations
g[u,n]: location or other user-specific side information
Location can be unavailable, inaccurate, stale, or misaligned.
Candidate scoring is conditioned on every active VUE.
Whose candidate list is it?
Multiple visible vehicles
Sensing + user side information
VUE-specific Top-K beams
Notes: Now remove the single-target assumption. With multiple visible vehicles, the prediction must be conditioned on the intended VUE, often using location or another side-information cue.

## Slide 6: Sensing-Target-to-User Association
Sensing observes physical vehicles, while beam management serves VUE identities.
A visible vehicle may not be active; the intended VUE may be unobserved; several targets may be plausible.
SENSING DOMAIN
Physical vehicles
Detections
Perception tracks
Target-level beam posteriors
COMMUNICATION DOMAIN
VUE identities
SSB / CSI-RS measurements
User-specific downlink
Which sensing target provides candidate beams for VUE u?
Notes: Emphasise the domain mismatch: perception names physical targets, while communication schedules VUE identities. This slide defines the association problem; it does not yet propose the tracker.

## Slide 7: Research Objectives and Contributions
Objective Reduce CSI-RS measurement overhead while preserving user-specific beam-management decisions.
Perception → Association → User-specific beam management
1 Distributed multimodal BEV perception for joint vehicle detection and beam prediction
Multi-view cameras + BS-local ISAC yield vehicle detections and per-target beam posteriors.
2 Measurement-assisted target-to-user association and tracking
VUE-indexed beam measurements establish credible UE-track pairs.
3 NR-oriented end-to-end evaluation
Sensing use, fallback, CSI-RS overhead, and effective user rate are evaluated together.
Notes: State the three contributions in order: joint BEV perception and beam prediction, measurement-assisted association and tracking, then end-to-end communication evaluation.

## Slide 8: System Model
01
What information is available to the BS, and how does a beam candidate affect user rate?
Notes: Transition to the system model. The next three slides define what information is available and what a valid beam-management action must respect.

## Slide 9: Network Architecture and Information Domains
Target BS b makes local decisions; neighbours only extend sensing coverage.
Communication: identified VUEs u ∈ U_b[n] | Sensing: unlabelled physical targets
U_b[n]: VUEs served by b • N_b: sensing-only neighbours • BEV: target-BS-centred
Notes: Define the local architecture before introducing sensing equations. The target BS serves the VUE set U_b[n] and makes every communication decision. Neighbouring nodes only add camera viewpoints. The key distinction is that communication identifiers refer to VUEs, whereas sensing observes unlabelled physical targets; all evidence is aligned in the target-BS BEV frame.

## Slide 10: ISAC Sensing Model
Known ISAC symbols enable BS-local extraction of dynamic vehicle evidence from static clutter.
H̃_{b,n} = Ĥᵉᶜʰᵒ_{b,n} − Ĥˢᵗᵃ_b → Z_{b,n}(ρ, θ, ν) = Tᴿᴬᴰ(H̃_{b,n}), |Z_{b,n}|² > ηᶜᶠᴬᴿ_{b,n}
Output: P_{b,n} = {(q_{b,m,n}, a_{b,m,n})}ᵐ⁼¹ᴺ ᵖᶜ_{b,n}
Known transmission
xᶳᵉⁿ_{b,n}[p,l] = √Pᶳᵉⁿ_{b,n} fᶳᵉⁿ_{b,n}[p,l] sᶳᵉⁿ_{b,n}[p,l]
Echo model
yᵉᶜʰᵒ_{b,n}[p,l] = (Hˢᵗᵃ_b[p] + Hᵈʸⁿ_{b,n}[p,l]) xᶳᵉⁿ_{b,n}[p,l] + zᶳᵉⁿ_{b,n}[p,l]
Notes: Follow the physical sensing chain. Known ISAC symbols are transmitted through a sensing beam. The echo consists of static and vehicle-related dynamic components. After estimating and subtracting the static background, range-angle-Doppler processing and CFAR retain the cells that form the BS-local point cloud P_b,n.

## Slide 11: Downlink Communication Model
From multi-user data streams to CSI-RS-based equivalent-channel feedback.
3. Hybrid RZF construction
Fᴿᶠ_b[n] = [fᶜˢᴵ_{b,k*_{b,u₁,n}}, …, fᶜˢᴵ_{b,k*_{b,u|𝒰_b[n]|,n}}]
Vᴿᶻᶠ_b[n] = Ĥᵉᶠᶠᴴ_b[n](Ĥᵉᶠᶠ_b[n] Ĥᵉᶠᶠᴴ_b[n] + λ_b I)⁻¹D_b[n]
Wᴿᶻᶠ_b[n] = Fᴿᶠ_b[n]Vᴿᶻᶠ_b[n]
1. Multi-user downlink
x_{b,n} = Σ_{u∈𝒰_b[n]} √P_{b,u,n} w_{b,u,n} s_{b,u,n}
2. CSI-RS scan over a candidate set |𝒞_{b,u,n}| = K
yᶜˢᴵ_{b,u,k,n}[l] = √Pᶜˢᴵ_{b,k,n} (hᴴ_{b,u,n}fᶜˢᴵ_{b,k}) c_{b,k,n}[l] + zᶜˢᴵ_{b,u,k,n}[l] , hᵉᵠ_{b,u,k,n} = hᴴ_{b,u,n}fᶜˢᴵ_{b,k}
k*_{b,u,n} = arg max_{k∈𝒞_{b,u,n}} γ̂ᶜˢᴵ_{b,u,k,n} , ĥᵉᵠ_{b,u,k*,n} = Corr(yᶜˢᴵ_{b,u,k*,n}, c_{b,k*,n})
Notes: First, the target BS transmits independent data streams to all VUEs. For every VUE, CSI-RS beams are then scanned only within the candidate set C, whose width is K. The VUE selects the measured beam with the largest reported CSI-RS quality and estimates its equivalent channel by correlating the reference observation with the known CSI-RS symbol. These feedback-based equivalent-channel estimates build the RF beam matrix and the digital RZF precoder; thus sensing can narrow C but never replaces CSI-RS feedback.

## Slide 12: Downlink Communication Model
The selected hybrid precoder determines both downlink quality and beam-management cost.
3. Beam-management resources and effective rate
τᵗᵒᵗ_{b,n} = τˢˢᴮ_{b,n} + τᶜˢᴵ⁻ᴿˢ_{b,n} + τᶜᵗʳˡ_{b,n} + τᵈᵃᵗᵃ_{b,n}
τᶜˢᴵ⁻ᴿˢ_{b,n} = Σ_{e∈𝓔_b[n]} ⌈K_e/M⌉δᵖʳᵒᵇᵉ , ηᵈᵃᵗᵃ_{b,n} = τᵈᵃᵗᵃ_{b,n}/τᵗᵒᵗ_{b,n}
Rᵉᶠᶠ_{b,u,n} = ηᵈᵃᵗᵃ_{b,n}Rᴰᴸ_{b,u,n} = ηᵈᵃᵗᵃ_{b,n}B_bηᴰᴸ_b log₂(1 + γᴿᶻᶠ_{b,u,n})
1. Precoded received signal
y_{b,u,n} = √P_{b,u,n} hᴴ_{b,u,n}wᴿᶻᶠ_{b,u,n}s_{b,u,n}
+ Σ_{v∈𝒰_b[n],v≠u} √P_{b,v,n} hᴴ_{b,u,n}wᴿᶻᶠ_{b,v,n}s_{b,v,n} + z_{b,u,n}
2. Post-RZF SINR and achievable rate
γᴿᶻᶠ_{b,u,n} = P_{b,u,n}|hᴴ_{b,u,n}wᴿᶻᶠ_{b,u,n}|² / [Σ_{v≠u}P_{b,v,n}|hᴴ_{b,u,n}wᴿᶻᶠ_{b,v,n}|² + σ²_{b,u,n}]
Rᴰᴸ_{b,u,n} = B_bηᴰᴸ_b log₂(1 + γᴿᶻᶠ_{b,u,n})
Notes: The hybrid RZF precoder from the previous slide now determines the received signal: desired data, residual multi-user interference, and noise. This produces the post-RZF SINR and the gross downlink rate. Separately, measuring K_e CSI-RS beams consumes resource in acquisition event e; after SSB, CSI-RS, control, and data allocations, eta-data is the remaining data fraction. Effective rate multiplies gross rate by this remaining fraction, exposing the beam-quality versus measurement-overhead trade-off.

## Slide 13: Design Requirements
A sensing-assisted beam-management policy must respect three information boundaries.
No oracle VUE identity · No direct service-beam declaration
1 TARGET-LEVEL PREDICTION Predict beams for an observed physical target, not a known VUE. 2 MEASUREMENT-GROUNDED ASSOCIATION Establish which perception track belongs to each VUE. 3 MEASURED SERVICE-BEAM SELECTION Use sensing to narrow CSI-RS candidates; use measured quality to select service.
Notes: Use these requirements as guardrails: target observability, association correctness, and conservative fallback when the evidence is insufficient.

## Slide 14: Proposed Framework
02
How does unbound sensing evidence become a VUE-specific CSI-RS decision?
Notes: Introduce DMSA-BM as the framework that connects perception evidence to a user-specific candidate measurement decision.

## Slide 15: DMSA-BM Architecture
Multimodal observations → detections and beam posteriors → physical-target tracks → VUE-track associations → CSI-RS candidates
1 DISTRIBUTED MULTIMODAL PERCEPTION
Cameras + BS-local ISAC
Vehicle detections
Per-target beam posteriors
2 IMM-BASED TRACKING
CV and CT motion models
Detection-to-track assignment
Physical-target continuity
3 TARGET-TO-USER ASSOCIATION
VUE-indexed beam measurements
One-to-one matching
Accepted or unmatched
4 CANDIDATE MEASUREMENT
Accepted + observed
Top-K predicted beams
Otherwise
SSB-guided refinement
Notes: Walk left to right through the architecture: distributed sensing, BEV fusion, joint target output, tracking, association, and candidate selection.

## Slide 16: Cross-Node Fusion
Cross-node attention selects complementary viewpoints at each BEV location while preserving the target-BS perspective.
Target-BS-conditioned queries preserve the serving-link view; geometry-aware keys distinguish node locations; masks exclude invalid projections.
Target-BS BEV
Node 1 BEV
Node 2 BEV
···
Validity masks
GEOMETRY-AWARE
MASKED ATTENTION
αⱼ(x) = softmaxⱼ
[q(x)ᵀkⱼ(x)/√d + b(gⱼ→b)]
Target-BS-centred
distributed camera BEV
Neighbouring evidence dominates only where valid.
Notes: Explain why neighbouring viewpoints improve observability without creating additional communication cells. All evidence is fused in the target-BS BEV frame.

## Slide 17: Multimodal Fusion
Gated local and global attention adapt camera–ISAC fusion to spatial and scene-wide observation conditions.
The fusion weights are learned from sensing features; availability masks only exclude missing inputs.
CAMERA BEV
Semantics and visibility
ISAC BEV
Complementary geometry
GATED ATTENTION
βq(x) ∝ exp
[ℓlocal,q(x) + ℓglobal,q]
Availability mask
FUSED BEV
Local weights respond to occlusion and sparsity.
Global weights respond to illumination and visibility.
Notes: Describe local camera and ISAC fusion as complementary inputs before cross-node BEV fusion.

## Slide 18: Joint Detection and Beam Prediction
A shared BEV representation produces vehicle detections and a per-target posterior over 192 CSI beams.
Detection output r̂ᵢ, attributes, confidence Beam output pᵢ = softmax(logits at r̂ᵢ) Training Top-1 cross-entropy Use Full posterior retained for ranking
Notes: Highlight the joint output: vehicle detections and a beam posterior for every detected target, rather than a beam chosen without a physical target.

## Slide 19: IMM-Based Physical-Target Tracking
IMM estimation maintains physical-target continuity across straight and turning motion.
CV model
x^(CV) = [x, y, v_x, v_y]^T
CT model
x^(CT) = [x, y, v, ψ, ω]^T
Model-posterior update
μ^(ℓ)_(r,n) = [Λ^(ℓ)_(r,i,n) μ̄^(ℓ)_(r,n)] / [Σ_(j∈{CV, CT}) Λ^(j)_(r,i,n) μ̄^(j)_(r,n)]
μ̄: model probability after mixing
μ^(ℓ)_(r,n) ∝ Λ^(ℓ)_(r,i,n) μ̄^(ℓ)_(r,n)
Mix → model-conditioned filtering → likelihood reweighting → fused physical-target state
Notes: Introduce the tracker as a physical-target state estimator, not a VUE-identity estimator. Contrast the CV and CT state vectors, then explain that innovation likelihood updates the model posterior. Use the bottom diagram only to orient the IMM cycle. Predicted-only tracks preserve continuity but cannot reduce the CSI-RS scan.

## Slide 20: Measurement-Grounded Target–User Association
Beam-measurement agreement links a VUE to a currently observed physical track.
1 Compatibility from a VUE-indexed beam measurement
c^assoc_(u,r,n) = − log[p^obs_(r,n)(κ_(b,u,n))+ε] / log M_CSI
Lower cost ⇔ stronger agreement between the VUE measurement and the current track posterior.
2 Partial one-to-one assignment with an unmatched option
σ̂ = arg min_σ Σ_(u∈U^evt_b[n]) c^assoc_(u,σ(u),n), σ(u)∈R^obs_(b,n) ∪ {∅}
Feasible edges: current observation + SSB-parent consistency; real tracks are one-to-one.
3 Accept only when the match is confident
A_(u,r,n) = 1{ c^assoc_(u,r,n) ≤ τ_assoc, Δ_(u,r,n) ≥ τ_margin }
∅ and Δ prevent forced ambiguous matching.
Notes: Explain the three equations in order: beam-measurement compatibility cost, partial one-to-one assignment with an unmatched option, and cost-plus-margin acceptance. Stress that the procedure uses a conventional VUE-indexed measurement and a current track posterior, without user location or ground-truth identities.

## Slide 21: Association-Gated Beam Candidate Selection
A sensing posterior reduces CSI-RS scanning only when the VUE–track mapping is accepted and current.
1 Candidate-use gate
G_(u,n) = A_(u,r,n), if π_(b,n)(u) = r ∈ R^obs_(b,n)
G_(u,n) = 0, otherwise
A predicted-only track gives G=0 and cannot reduce the measurement set.
2 Measurement-set policy
C_(b,u,n) = TopK_Kscan(p^obs_(π_(b,n)(u),n)), G_(u,n)=1
C_(b,u,n) = C^ref_(b,u,n)(K_ref), G_(u,n)=0
Adaptive width: choose the smallest Kscan whose leading posterior mass reaches ζ.
Measurement safeguard
The posterior ranks CSI-RS candidates; the service beam is selected from measured CSI-RS quality.
Notes: Explain that candidate reduction requires both an accepted target-to-user association and a current observation. A predicted-only track makes the gate zero and triggers conventional SSB-guided refinement. The posterior ranks measurement candidates only; the service beam remains selected from measured CSI-RS quality.

## Slide 22: Algorithm Summary
The framework separates sensing computation from air-interface measurement cost.
Scaling drivers Views and BEV resolution · targets and tracks · assignment size · M_CSI · K_scan
1 Construct distributed multimodal BEV features. 2 Decode detections and beam-class posteriors. 3 Predict, assign, and update physical-target tracks. 4 Reassociate only when an association event occurs. 5 Select sensing-derived or SSB-guided CSI-RS candidates.
Notes: Summarise the full decision loop and identify the guarded interface between sensing evidence and CSI-RS measurement.

## Slide 23: Experimental Evaluation
03
Does the complete decision chain improve communication performance after measurement cost is included?
Notes: Transition from method to evidence. The question is whether the complete chain improves the stated communication operating point.

## Slide 24: Experimental Setup
A common multimodal and communication protocol links perception results to effective user rate.
SCENARIOS
Four roadside BSs
Clear
Rain/Fog
Night
Disjoint train, validation, and test sequences
MULTIMODAL DATA
Target-BS cameras
Neighbouring-node cameras
BS-local ISAC point clouds
Vehicle trajectories
Ray-traced channels
RADIO PROFILE
48 SSB beams
192 CSI-RS beams
SSB period 100 ms
CSI-RS period 20 ms
Common power, noise, Doppler, RZF, and overhead accounting
EVALUATION CHAIN
Detection
→ Beam ranking
→ Association-conditioned use
→ CSI-RS overhead
→ Effective user rate
Rain/Fog margin is a fixed test-tuned operating point.
Notes: Briefly state the scenario, modalities, channel and protocol assumptions, and the metrics reported on the following slides.

## Slide 25: Perception and Beam Prediction
Distributed multimodal attention improves target availability without uniformly dominating every beam-ranking metric.
Chart: 
| AP@2m | Recall@2m | Beam Top-1 | Beam Top-4
Local camera–ISAC fusion | 74.35 | 79.53 | 71.54 | 94.66
Distributed multimodal attention | 78.73 | 81.51 | 71.13 | 94.13
Blue Distributed multimodal attention
Gray Local camera–ISAC fusion
Proposed
AP 78.73%
Recall 81.51%
Top-4 power ratio 97.01%
Local fusion
Top-1 71.54%
Top-4 94.66%
Target observability and beam ranking are distinct objectives.
Notes: Explain the perception and per-target beam-prediction results, distinguishing detection quality from communication-level decisions.

## Slide 26: Cooperative Sensing Nodes
Additional roadside viewpoints primarily improve detection and localisation.
Blue AP@2m Orange Recall@2m Olive Beam Top-4@2m Fixed trained model Available nodes varied only at test time 0 → 5 nodes AP 38.59% → 80.41% Recall 52.34% → 83.15% Beam Top-4 approaches saturation.
Chart: Available nearby sensing nodes
| 0 | 1 | 2 | 3 | 4 | 5
AP@2m | 38.59 | 50.3 | 56.42 | 58.39 | 71.4 | 80.41
Recall@2m | 52.34 | 57.39 | 60.78 | 62.45 | 74.25 | 83.15
Beam Top-4@2m | 91.58 | 92.03 | 94.09 | 94.63 | 95.3 | 95.4
Notes: Explain the contribution of cooperative sensing nodes under the reported viewpoints and conditions.

## Slide 27: Communication Performance
DMSA-BM achieves the highest reported effective user rate with the lowest CSI-RS overhead among the compared schemes.
CSI-RS overhead
SSB-guided, Kref = 4 1.90%
SSB-guided, Kref = 12 5.71%
DMSA-BM 1.56%
Sensing use
Clear 76.35% · Rain/Fog 56.65% · Night 30.07%
Fallback: retain SSB-guided refinement when sensing is not used.
Chart: 
| SSB K=4 | SSB K=12 | DMSA
Effective user rate | 142.248 | 115.89 | 146.332
Notes: Use this slide to read the communication result directly: DMSA-BM combines the lowest reported CSI-RS overhead with the highest reported effective user rate among the compared schemes.

## Slide 28: Ablation and Tracking Results
Local multimodal complementarity provides most of the gain; distributed sensing improves the final operating point.
CSI-RS overhead Camera 1.86% ISAC 1.81% Local fusion 1.80% DMSA-BM 1.56% Tracker check IMM 146.332 KF-CV 146.373 KF-CT 145.880 Mbps Similar rates do not establish universal IMM superiority.
Chart: Mean effective user rate (Mbps)
| Camera-only | ISAC-only | Local camera–ISAC | DMSA-BM
Effective user rate | 138.868 | 142.522 | 143.701 | 146.332
Notes: Interpret ablation and tracker comparisons cautiously: the result identifies the reported operating point rather than a universal ordering.

## Slide 29: Conclusion
04
What has been established, and what remains before deployment?
Notes: Recap what has been established before the final slide: the association gate is the bridge between target-level sensing and VUE-specific measurement.

## Slide 30: Conclusions and Future Work
Distributed sensing becomes useful for beam management through a user-specific measurement interface.
NEXT STEPS Real-world validation Protocol-level NR evaluation Online and domain adaptation Cooperative multi-BS association QUESTIONS AND DISCUSSION
□ Distributed multimodal BEV perception jointly detects vehicles and ranks per-target CSI beams. □ IMM tracking preserves physical-target continuity without treating a track as a VUE identity. □ Beam measurements establish target-to-user associations; only accepted, currently observed pairs reduce CSI-RS scanning. □ Under the stated operating point, DMSA-BM achieves 146.332 Mbps with 1.56% CSI-RS overhead.
Notes: Close with the central conclusion and the stated future-work directions, then pause for questions.